| Title | Use electronic test equipment |
| --- | --- |
| Level | 3 | Credits | 6 |

| Purpose | This unit standard covers the use of test equipment widely employed in the electronics industry and laboratories to measure electronic circuits. People credited with this unit standard are able to: – demonstrate and apply knowledge of electrical measuring instruments; – demonstrate knowledge of measurement accuracy and calibration when testing electronic equipment; – use digital and analogue multimeters; – use a bench power supply; – use a function generator; – use an oscilloscope; and – use logic probes. |
| --- | --- |

| Classification | Electronic Engineering > Core Electronics |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	References

Electricity (Safety) Regulations 2010;

Electricity Act 1992;

EWRB Rules of the Board and Teaching Guidelines available at www.ewrb.govt.nz;

Health and Safety at Work Act 2015;

and all subsequent amendments and replacements.

2	Definitions

a.c. – alternating current.

d.c. – direct current.

FSD – full scale deflection.

Industry practice – those practices that competent practitioners within the industry recognise as current industry best practice.

RMS – root mean square.

3	Range

a	Electrical, radiation, and workshop or laboratory safety practices are to be observed at all times.

b	All measurements are to be expressed in Système Internationale (SI) units and multipliers.

c	All activities and evidence presented for all outcomes and performance criteria in this unit standard must be in accordance with:

i	legislation;

ii	company policies and procedures;

iii	ethical codes;

iv	Standards – may include but are not limited to those listed in Schedule 2 of the Electricity (Safety) Regulations 2010;

v	EWRB Rules of the Board;

vi	safe and sound practice;

vii	applicable site, company, and industry practice.

Outcomes and performance criteria

Outcome 1

Demonstrate and apply knowledge of electrical measuring instruments.

Range	a.c. and d.c. voltage, a.c. and d.c. current, resistance, continuity, insulation resistance.

Performance criteria

1.1	Describe analogue and digital electrical measuring instruments in terms of their principles of operation and their applications.

Range	instruments – multimeter, clip-on ammeter, insulation tester, d.c. ammeter, d.c. voltmeter, ohmmeter;

applications – a.c. and d.c. voltage and current, resistance, insulation, continuity, diode testing, use of series and parallel shunts, battery, potentiometer, other specialised functions.

1.2	Select instruments to match the type of measurement and inspect to ensure safety before testing.

1.3	Set and connect instruments in accordance with manufacturers’ specifications and in a manner that causes no danger to persons, instruments, or the equipment under test.

1.4	Take and record measurements in accordance with industry practice to ensure that components under test and test equipment are not damaged and personnel are not injured.

1.5	Determine the approximate tolerance for each measurement in accordance with industry practice.

Outcome 2

Demonstrate knowledge of measurement accuracy and calibration when testing electronic equipment.

Performance criteria

2.1	Describe sources of measurement error.

Range	parallax, interpolation, analogue instrument accuracy as % of FSD, digital meter error as sum of % of reading plus digit error, meter loading of circuit measured, effect of waveform, calibration hierarchy, input levels.

2.2	Describe the differences between instruments reading true RMS and a.c. rectified average with reference to measurements of sine and square waves.

2.3	Describe the principle and use of voltage probes in measurement of electronic circuits.

2.4	Identify sources for regular calibration of instruments.

Outcome 3

Use digital and analogue multimeters.

Range	measurements of – a.c. and d.c. voltage and current, resistance.

Performance criteria

3.1	Explain measurement accuracy variance when using meters in high impedance low currents circuits.

3.2	Take a.c. and d.c. measurements, and calculate and record percentage errors.

Range	analogue error as a percentage of FSD; digital error as a percentage of reading plus digit error over a frequency range of d.c to 100kHz.

3.3	Explain safety classification rating of meters.

Outcome 4

Use a bench power supply.

Performance criteria

4.1	Explain the purpose of all controls and safety features are explained.

4.2	Use power supply to energise electronic circuits to specified levels.

Outcome 5

Use a function generator.

Performance criteria

5.1	Explain the purpose of all controls and safety features.

5.2	Inject Sine, square, and sawtooth signals at specified levels into electronic circuits in a manner that does not affect the circuit operation.

Outcome 6

Use an oscilloscope.

Range	waveforms – sine, square, sawtooth, more complex with spikes;

measurements – wave shape, d.c. voltage, peak-to-peak voltage, spike voltage, frequency, phase.

Performance criteria

6.1	Outline the principle of operation of a basic oscilloscope and its use for measurement purposes.

6.2	Describe limitations and safety precautions to be observed in the use of an oscilloscope.

6.3	Calibrate for voltage and frequency using internal calibration procedure in accordance with instrument manual.  Calibration includes high impedance or high voltage probe.

Range	calibration includes – high impedance, high voltage probe.

6.4	Confirm suitability or otherwise of oscilloscope for the type of measurement with reference to input voltage limitation, frequency, impedance, and earthing.

6.5	Ensure connection of oscilloscope to circuit does not affect circuit operation or measurement accuracy.

6.6	Adjust frequency and trigger points to produce steady display of waveforms.

6.7	Take measurements and recorded together with an indication of the expected degree of accuracy.

Outcome 7

Use logic probes.

Performance criteria

7.1	Outline the principles of operation of logic probes to display bus and logic gate states.

7.2	Examine logic states of bus and gates in accordance with instrument instructions.

| Replacement information | This unit standard replaced unit standard 8199. |
| --- | --- |

| Planned review date | 31 December 2025 |
| --- | --- |

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 24 November 2003 | 31 December 2011 |
| Rollover and Revision | 2 | 22 August 2008 | 31 December 2012 |
| Review | 3 | 21 July 2011 | 31 December 2022 |
| Review | 4 | DD MM 2020 | N/A |

| Consent and Moderation Requirements (CMR) reference | 0003 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.

Comments on this unit standard

Please contact The Skills Organisation reviewcomments@skills.org.nz if you wish to suggest changes to the content of this unit standard.

# Comments

7 items to measure x 5 PCs = 35 assessments.  Confirm that we are not over assessing.

What is the expectation here? Do we want learners to describe everything on this list? Or, for example, is a minimum of 4 instruments, and 5 applications enough?

I agree.  6 instruments x 12 applications x the 7 items to measure in the Outcome Range = 504 tests?

The range of applications in PC1.1 looks like a double up of the OC1 Range statement too, do you need it here?

What is the expectation here? Do we want learners to describe everything on this list?

Consider adding more tests in OC3 to OC7 compared to theory OC1 and OC2.

Please clarify. Is it:

A) a.c voltage + current + resistance, d.c voltage + current + resistance; or

B) a.c. and d.c. voltage and current, + resistance?

Yes, please clarify.  I think this is:

ac voltage, dc voltage, ac current, dc current, resistance

Must learners be assessed on everything in this list? 4 types of waveforms x 6 measurements x 7 PCs = 168 tests.