| Title | Carry out soldering and de-soldering of printed circuit board mounted components and printed circuit board repair |
| --- | --- |
| Level | 3 | Credits | 8 |

| Purpose | This unit standard covers soldering, de-soldering, and repair of printed circuit boards (PCB) for electronics technicians. People credited with this unit standard are able to: maintain soldering and de-soldering equipment; de-solder and solder using soldering irons and soldering stations; de-solder and solder using airflow equipment; and bridge and repair broken PCB. |
| --- | --- |

| Classification | Electronic Engineering > Electronic Installation and Maintenance |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	References

Electricity Act 1992;

Electricity (Safety) Regulations 2010;

EWRB Rules of the Board and Teaching Guidelines available at www.ewrb.govt.nz;

Health and Safety at Work Act 2015;

IPC-A-610E Acceptability of Electronic Assemblies;

and all subsequent amendments and replacements.

2	Definitions

Industry practice – those practices that competent practitioners within the industry recognise as current industry best practice.

PCB – printed circuit board.

SMD – surface mounted device.

4	Range

a	Soldering equipment – soldering irons, airflow soldering equipment.

b	Electrical, radiation, and workshop or laboratory safety practices are to be observed at all times.

c	All soldering work must be carried out using only lead-free solder.

d	All activities and evidence presented for all outcomes and performance criteria in this unit standard must be in accordance with:

i	legislation;

ii	company policies and procedures;

iii	ethical codes;

iv	Standards – may include but are not limited to those listed in Schedule 2 of the Electricity (Safety) Regulations 2010;

v	EWRB Rules of the Board;

vi	safe and sound practice;

vii	applicable site, company, and industry practice.

Outcomes and performance criteria

Outcome 1

Maintain soldering and de-soldering equipment.

Performance criteria

1.1	Ensure soldering iron tips are tinned, clean, and the correct shape.

1.2	Ensure tests confirm that the soldering iron temperature control system is operating in accordance with the manufacturer’s specifications, and conforms to electrical safety requirements.

1.3	Ensure nozzles for airflow soldering and de-soldering equipment are blockage free and clean.

Range	airflow equipment includes one of the following – positive pressure, vacuum.

1.4	Ensure hoses of airflow soldering and de-soldering equipment are damage free.

1.5	Ensure airflow soldering and de-soldering equipment is operating to manufacturer’s specifications.

Range	temperature, vacuum and/or pressure.

1.6	Ensure airflow soldering and de-soldering equipment conforms to electrical safety requirements.

Outcome 2

De-solder and solder using soldering irons and soldering stations.

Performance criteria

2.1	Complete de-soldering and removal of through-hole and SMDs from PCB within agreed timeframe using soldering irons and soldering stations.

Range	through-hole and surface mount components include – resistors, capacitors, diodes, transistors, integrated circuits, inductors, wires, lugs, connectors.

2.2	Complete replacement and soldering of components onto PCB within agreed timeframe using soldering irons and soldering stations.

2.3	Ensure adjacent components are undamaged and unaffected by soldering and de-soldering operations.

Range	no melting, discolouring, inadvertent removal, heat damage, short circuit tracks.

2.4	Ensure PCB is free from damage caused by use of soldering irons and soldering stations.

Range	no bubbled board, burns, lifted tracks and lands, stressed tracks and lands, cut and broken tracks and lands, short circuits, board leakage.

2.5	Ensure soldered PCB is free from flux residue.

2.6	Ensure solder used matches component and board type.

Range	paste, conventional solder wire.

2.7	Ensure soldering iron and soldering station temperature is correct for type of PCB and component.

2.8	Ensure soldered and de-soldered PCB is reliable and operational to manufacturer’s specifications.

Outcome 3

De-solder and solder using airflow equipment.

Performance criteria

3.1	Complete de-soldering and removal of through-hole and surface mount components from PCB within agreed timeframe using airflow soldering and de-soldering equipment.

Range	through-hole and surface mount components include – resistors, capacitors, diodes, transistors, integrated circuits, inductors, wires, lugs, connectors.

3.2	Complete replacement and soldering of components onto PCB within agreed timeframe using airflow soldering and de-soldering equipment.

3.3	Ensure adjacent components are undamaged and are unaffected by soldering and de-soldering using airflow soldering and de-soldering equipment.

Range	no melting, discolouring, inadvertent removal, heat damage, short circuit tracks.

3.4	Ensure PCB is free from damage caused by use of airflow soldering and de-soldering equipment.

Range	no bubbled board, burns, lifted tracks and lands, stressed tracks and lands, cut and broken tracks and lands, short circuits, board leakage.

3.5	Ensure soldered PCB is free from flux residue.

3.6	Ensure solder used matches component and board type.

Range	paste, resin core solder wire.

3.7	Ensure airflow soldering and de-soldering equipment temperature is correct for type of PCB and component.

3.8	Ensure soldered and de-soldered PCB is reliable and operational to manufacturer’s specifications.

Outcome 4

Bridge and repair broken PCB.

Performance criteria

4.1	Identify cracks and breakages in PCB and fix within agreed timeframe.

4.2	Ensure repaired PCB withstands physical stress of normal wear and tear for type of product under repair.

4.3	Ensure repaired PCB is free from charcoal, burns, and holes.

4.4	Ensure repaired tracks on PCB deliver current carrying requirements of circuit.

4.5	Ensure PCB with bridged and repaired tracks is free from short circuits and leakage.

4.6	Ensure PCB with bridged and repaired tracks is free from dry joints.

4.7	Ensure PCB with bridged and repaired tracks meets manufacturer’s operating specifications.

| Planned review date | 31 December 2025 |
| --- | --- |

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 29 October 1996 | 31 December 2011 |
| Revision | 2 | 3 April 2001 | 31 December 2011 |
| Review | 3 | 24 November 2003 | 31 December 2012 |
| Review | 4 | 21 July 2011 | 31 December 2022 |
| Review | 5 | DD MM 2020 | N/A |

| Consent and Moderation Requirements (CMR) reference | 0003 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.

Comments on this unit standard

Please contact The Skills Organisation reviewcomments@skills.org.nz if you wish to suggest changes to the content of this unit standard.